## Slide 1: UAV Test Benches for Flight James Walker, Michael Heim, Bapi Surampudi, Pablo Bueno, Sidney Chocron,
7/24/21

## Slide 2: SwRI Flight Dynamics Model and Test Bench
We have a flight dynamics model written (full 6 DOF) in Fortran that will provide some test benches – it is essentially the same as before (you may wish to consult previous slide sets).
There are now four dynamic test benches, described here.
Each one is scored and is worth around 300 to 400 points.
We expect to add up these points.
Information from the trim state computations is used in these test benches. That test bench can be used to design vehicles based on their expected trim state performance.
However, each of these test benches involves flight and hence controls.
We will describe the autopilot and how you can interact with it.

## Slide 3: SwRI Flight Dynamics Model Comments
Comments: most physics is in the FDM. What’s not there is
  The vehicle does not interact with itself it at this point. That means, for example, that we are not computing induced flow from the propellers and examining how that induced flow influences other propellers or body surfaces or wing surfaces. We are also not including how wings deflect flow that may affect trailing surfaces.
    Example of how this omission could affect your design: some aerobatic aircraft and RC aircraft with one propeller can hover when the aircraft orients itself pointing upward. Our solver does not find a trim state for an aircraft like this (though if you build one and look at the trim state attempt you will see it correctly orients the aircraft but then does not find a trim state) because the way the real aircraft achieves a hover is by the induced flow from the propeller interacting with the ailerons to match (in the opposite direction) the torque on the plane from the propeller.
  There are no rate dependent terms (sometimes called damping coefficients) which are forces due to transient motion in the air. These are not present in trim states but can/do occur in flight when an aircraft is changing its angle of attack, for example.

## Slide 4: The Autopilot
We have developed an autopilot that can fly most aircraft. We’ve tried it out on quadcopters, octacopters, decacopters, planes, etc.
You do not need to identify the control channel connections, the autopilot will figure it out. (You do need to identify control channels as with the trim FDM calculations, but you don’t need to provide any additional information.)
The autopilot is based on the linear quadratic regulator (LQR) solution and trim states. To fly, you need a trim state. The LQR helps you get back to the trim state. Flying is not the same as a trim state, as you will discover by setting a quadcopter in a fixed trim state and letting it go.
A current weakness in our autopilot is that we are only computing lateral movement trim states, not banked turns. Thus, for now, some vehicles cannot take curves very fast. It depends on your design – some can. (Hopefully in the future this will be addressed.)

## Slide 5: More on the Autopilot
You can influence the autopilot through five input variables. These variables, in the .inp file, are
  control%Q_position ! The XYZ deviation weight (world frame)
  control%Q_velocity ! The UVW deviation weight (body frame, but makes no difference)
  control%Q_Angular_velocity ! The PQR deviation weight (body frame; same as world frame)
  control%Q_angles ! The quaternion connection world to body frame deviation weight
  control%R ! The weight on the control variables.
We compute a linearization around the trim state, and then solve the LQR problem, minimizing the time integral from 0 to infinity of xTQx + uTRu. Our Q above are along the diagonal and R is the constant R times the identity.
We have a matrix K of controls so that u = utrim + K(x – xtrim), where x is the state vector (U V W P Q R q1 q2 q3 X Y Z) (we drop q0).
The values of Q and R are only relative to each other, and the values can/do affect the results (but I have no simple explanations for how to choose them). Right now they are all set to 1 which has worked for many of our vehicles.

## Slide 6: Dynamic Test Bench 1: Rise and Hover
This test bench examines control during vertical flight of the vehicle as it rises from 0 to 200 meters and then hovers.
The goal speed for rise is 10 m/s, but we do not include the actual speed in the score.
You need to reach 200 meters, otherwise no points (you need to be at 200 plus or minus 2 meters altitude when you complete).
The objective is to do this and hover (rise time counts) for 200 seconds: that’s 200 points.
If you can go for another 200 seconds you can get one point per second, up to 400 points. That’s the max.
You are done hovering when one battery reaches 20% charge left. (Sorry, don’t know how else to do it for multiple batteries: your time is up when the first battery reaches this state.)
control%i_flight_path = 4

## Slide 7: Dynamic Test Bench 2: Fly a Straight Line
This test bench examines control during level steady flight of the vehicle as it flies north.
You begin in a trim state of your choice (from the integral trim states) at an initial 200 meters altitude and then you fly north.
You pick your speed.
Your flight ends when one battery reaches 20% charge.
You need to fly at least 2 kilometers, otherwise no points.
The number of points is meters/10 up to 400 points (i.e., you will get 0 points or 200 to 400 points) minus 10 times your lateral error in meters.
  So if you wander off the flight path by 10 meters you lose 100 points (however, if you wander off this far you will likely wander off a lot more and end up with zero points).
control%i_flight_path = 1

## Slide 8: Dynamic Test Bench 3: Fly a Circle
This test bench examines control during level steady flight of the vehicle as it traverses a circle of diameter 1 km (so you need to fly 3.15 km to get points).
You begin in a trim state of your choice (from the integral trim states) at an initial 200 meters altitude and then you fly the circle.
You get to pick your speed (i.e., the trim state of your choice).
Your flight ends when one battery reaches 20% charge or you finish the circle.
If you fly the circle you get 300 points minus 50 times your lateral error in meters.
control%i_flight_path = 3

## Slide 9: Dynamic Test Bench 4: Racing Oval
This test is a racing oval. You go 1 km, then you turn around on a 250 meter radius circle, then you go 1 km and again turn around on a 250 m radius circle and come back to the same point. This course is 3.57 km long.
You begin in a trim state of your choice (from the integral trim states) at an initial 200 meters altitude and then you fly the course.
You get to pick your speed (i.e., the trim state of your choice).
Your flight ends when one battery reaches 20% charge or you finish the course.
Finishing the course is 200 points. Given a “standard” speed of 10 m/s to traverse the course, for every second less than 350 seconds you get a point.
  So if you go 20 m/s you end up with 375 points.
If you depart from the course path by 10 meters (laterally), you get zero points.
control%i_flight_path = 5

## Slide 10: Extra slide follows
Extra slide from DARPA PI meeting (next slide) – we show this as a reminder of where things are going.

## Slide 11: Types of Testbenches to Expect for First Hackathon
We envision a set of hackathon requirements similar in format to AIAA Design Build Fly competitions which we have helped run.
For example, it will look something like this (points from each test):
  Specification of a build and mass box that the vehicle must fit within. Build from our corpus.
  Test 1: Lift off, hover at a given altitude, and then land.
    Test 1A: Same maneuver with random gust. Points based on controllability.
  Test 2: For a specific “loosely” defined course, take off vertically, follow course, and land vertically. Must stay inside defined corridor. Points based on fastest time.
  Test 3: For a specific three-dimension curve (path) in space, must follow path in detail. Time does not matter, precision of following path does. Points based on excursions.
  Test 4: Within given corridors, take off with a specified cargo, deliver to a specified location, and return. Points based on some combination of time and precision.
  Test 5: Vertical takeoff, vertical landing, cruise altitude, straight course. Maximize distance.
  Test 6: (Hard test – so maybe not first hackaton): Takeoff to altitude, hit cruise, lose motor power (one motor? Two? All?). Try to minimize ground thump and control impact point.
  We have “perfect GPS” – i.e, you know where you are. Issue is aero design and controls.

## Slide 12: End of Slides